# Implementing Congestion Management with Redispatch Provisions

# Assumptions

# ReservationA-B = 100 MW from A to B

# TransactionA-B = 100 MW from A to B using ReservationA-B

Customer = B

Flowgate Impacts = 10 MW on Flowgate 1

Redispatch Requirement = 50 MW from Unit A1 to A2

If generators associated with Redispatch Requirement are Self-Dispatched:

- Call TLR 3.  IDC will curtail appropriate non-firm transactions from resources not offered to Market.  Activate Flowgate in Constraint Manager to initiate required Market Redispatch to remove non-firm market flow.  Continue until flow is maintained within Flowgate 1 limit or all non-firm transactions and non-firm market flows have been curtailed.  If all non-firm flows have been curtailed and remaining flows still exceed the Flowgate limit, move to next step.

- Call TLR 4.  SPP Reliability desk notifies Customer B of requirement to implement Redispatch Requirement.  Customer B must initiate the creation and submittal of an appropriate tagged schedule to facilitate the Redispatch Requirement through their Scheduling Agent pursuant to the applicable redispatch agreement.   Customer B or their Scheduling Agent will initiate the submittal of an Emergency Transmission Service request on the SPP OASIS for tagging purposes. If flows are maintained with the Flowgate limit, no further action is needed.  If flows still exceed the limit and no action has been taken to implement the redispatch, move to next step after 30 minutes, unless quicker action is required by system conditions.

- If the schedule necessary to meet the Redispatch Requirement has not been submitted and implemented, curtail/adjust TransactionA-B.  If flows still exceed the Flowgate limit, move to next step.  If at any time during TLR 4 the Redispatch Requirement is not met, TransactionA-B will be curtailed/adjusted before proceeding to TLR 5.

- Call TLR 5 to curtail necessary firm transactions and market flow on a pro-rata basis.  If at any time during TLR 5 the Redispatch Requirement is not met, TransactionA-B will be curtailed/adjusted before initiating further curtailments of other firm transactions.

If generators associated with Redispatch Requirement are Available for market dispatch:

- Call TLR 3.  IDC will curtail appropriate non-firm transactions from resources not offered to Market.  Activate Flowgate in Constraint Manager to initiate required Market Redispatch to remove non-firm market flow.  Continue until flow is maintained within Flowgate 1 limit or all non-firm transactions and non-firm market flows have been curtailed.  If all non-firm flows have been curtailed and remaining flows still exceed the Flowgate limit, move to next step.

- Call TLR 4.  If the total Dispatchable Range for generators involved in Redispatch Requirement is less than 50 MW or if offered ramp rates will not allow full affect of Redispatch Requirement within 15 minutes, SPP will notify Generator Owner A to effect appropriate Resource Plan changes.  Notify Customer B of requirement to implement Redispatch Requirement.  Customer B must initiate the creation and submittal of an appropriate tagged schedule1 to facilitate the Redispatch Requirement through their Scheduling Agent. Customer B or their Scheduling Agent will initiate the submittal of an Emergency Transmission Service request on the SPP OASIS for tagging purposes. If flows are maintained with the Flowgate limit, no further action is needed.  If flows still exceed the limit and no action has been taken to implement the redispatch, move to next step after 30 minutes, unless quicker action is required by system conditions.

- If the schedule necessary to meet the Redispatch Requirement has not been submitted and implemented or Generator Owner A cannot achieve the required Dispatchable Range and offered ramp rates, SPP will curtail/adjust TransactionA-B.  If flows still exceed the Flowgate limit, move to next step.  If at any time during TLR 4 the Redispatch Requirement is not met, TransactionA-B will be curtailed/adjusted before proceeding to TLR 5.

- Call TLR 5 to curtail necessary firm transactions and market flow on a pro-rata basis.  If at any time during TLR 5 the Redispatch Requirement is not met, TransactionA-B will be curtailed/adjusted before initiating further curtailments of other firm transactions.

# Footnotes

The tagged schedule must be a single schedule from A1 to A2.  Emergency Transmission Service will be required to deliver from A1 to A2. Emergency Transmission Service must be requested on the SPP OASIS pursuant to SPP Business Practice 1.12 guidelines.